## Slide 1: Designing an LTE Baseband MPSoC With a Novel Multi-Core HW/SW Platform Concept
Gerhard Fettweis, and
Emil Matus, Torsten Limberg, Markus Winter, Reimund Klemm, Marcel Bimberg, Marcos Tavares, Steffen Kunze
Vodafone Chair – TU Dresden
Talk at MPSoC 2009 in Savannah, GA
Notes: Design Goals

## Slide 2: SDR & Multimedia - Platform Requirements
Flexibility
  Different types of processors for different applications (GPPs, domain specific, ASIPs, ASICs)
  Modularity – build up system from established modules and specific components if necessary
Programmability
  Programmability in accepted language like C
  Real-Time capability
  Efficient integration of accelerator tasks in control code
  Programs should be binary compatible on similar architectures
Scalability
  Efficient interconnection of system components

## Slide 3: Terminology
Task
  Atomic execution unit typically for algorithm kernels
  Executed on a processing Element
  May have varying, but must have maximum execution time
  Tasks consume and produce chunks of data
(Real-Time) Thread
  Execution unit consisting of control code and task instances
  Executed on control processor
  Real-Time Threads have deadline
  Tasks from different threads have no data dependencies
  Threads may have synchronization points
Program
  Collection of Threads making a complete application

## Slide 4: The Task
CPU
CPU
DMA
PE
DMA
Global Memory
Task Start
Data Store
Task Execution
Data Load
Task End
Local Memory
Encapsulated task executions
  Data/programm locality
  Processing without interruption due to bus access
  Efficient utilisation of deeply pipelined global RAMs

## Slide 5: Programming Model – Problem Statement
Program: application to be executed
Threads: concurrent paths of execution within the program
Tasks: computational kernels consuming and producing chunks of data
  Tasks can have data dependencies
  Tasks can be executed on different kinds of processing elements (PE)
  In conventional systems, task synchronization produces huge scheduling overhead
Problem: How can efficient mapping of tasks and control code be realized?
Operating System
SoC
Program
Thread
Thread
t1
t2
t3
t4
t5
t6
t1
t2
t3
t4
t6
t5
CP
PE1
PE2
PE3
PE4
PE5
PE6
PE7
PE8
PE9
Notes: Software and Hardware Part of the system
PE is something like DSP, ASIP, ASIC
Problem – Tasks are usually not independent!
Usual way of mapping: Start Tasks, use Semaphores, Interrupts or other Sync mechanism
Motivation facts do not allow such technique

## Slide 6: Programming Model – Solution
Solution: “CoreManager” hardware unit which takes cares of:
  Dependency checking
  Local memory management of PEs
  Data transfers from and to local memories
  Task mapping to PEs
CP sends task descriptions to CoreManager
Communication makes use of standard NoC interface
 No synchronization interrupts
 OS scheduling eased
 Predictable results due to explicit use of local memories
Operating System
SoC
Program
Thread
Thread
t1
t2
t3
t4
t5
t6
t1
t2
t3
t4
t6
t5
CP
PE1
PE2
PE3
PE4
PE5
PE6
PE7
PE8
PE9
CoreManager
Notes: Local memories increase predicatbility since no caching needs to be taken into account.
Task Runtime is not deterministic for GPP PEs due to unknown cache state. But an upper runtime limit can be computed for the case of uninitialized cache.

## Slide 7: Programming Model – C++ Implementation
Threads are represented by C++ classes
Tasks may be C-functions or static C++ class members
class MyThread_t:
public RtThread_t {
private:
void _Execute ( );
int _status;
};
void MyThread_t::_Execute ( ) {
int i1[20], i2, o[20];
if ( _status == 0 )
task(t1, IN(i1, 4), IN(&i2, 4),
OUT(o, 4));
else
task(t2, IN(i1, 20), OUT(o, 20));
...
Thread Implementation
Thread Declaration
Task Declaration/
Implementation
Thread Instance Execution
Task Call
#pragma TASK_BEGIN
#pragma TASK_NAME t1
void t1(void *i1, void *i2, void *o) {
(int)o = (int)i1 * (int)i2;
}
#pragma TASK_END
int main() {
MyThread_t threadInstance;
threadInstance.Start ( );
return 0;
}
Notes: MyThread_t is derived from Thread base class
Task functions may contain inlined assembly code
Start function is declared in base class

## Slide 8: Hierarchy of Processing
Control Processor
Task Scheduler
“Core Manager”
Processing Elements
Multi Threading OS
Multi-Task MMU
Main Memory Buffer Ctrl.
Task Handling
Per Thread Control:
Task Main Execution
PE Task Queue Mgmt.
Task Execution
Granularity

## Slide 9: Task Scheduler: Task Run-Time Management
Data Dependency Check
Dynamic Memory Allocation
PE and DMA Allocation
DMA Transfers / Tasks
Memory deallocation
Task Decoding
Scheduling
Task List
Task Execution

## Slide 10: System Schematic
Processing
Element
Processing
Element
Processing
Element
CoreManager
Control
Processor
Processing
Element
Processing
Element
Processing
Element
Processing
Element
Processing
Element
Processing
Element
DMA
DMA
DMA
DMA
Software
Hardware
TaskTools
.cpp
.o
.o
.o
.lib
Interconnection
Control
Processor
Control
Processor

## Slide 11: Task Tools
.lib
.cpp
Task Splitter
.cpp
.c(pp)
.c(pp)
.c(pp)
CP C++
Compiler
PE C(++)
Compiler
PE C(++)
Compiler
PE C(++)
Compiler
.o
.o
.o
.o
Linker
.exe
Program and Threads, written in C++
Tasks written in C++, C or C with inline Assembly
Optimized algorithm kernels, written in C++, C or C with inline assembly
using

## Slide 12: CoreManager
DMA Controllers
Load
Prog.
Memory Allocator
Resource Allocation
Dependency Checker
In-Place Modification Handling
Task Description Unit
Cleanup Channels
Write
Data
Read
Data
NoC
NoC
PE Control
Processing Elements
CoreManager
  Dependency checking
  PE Allocation
    Memory Allocation
  Transfer Scheduling
  Execution Scheduling
  Resource Deallocation
RT-Extension
  Task Priorization
  Task Replacement
  Dynamic Iteration Count Reduction

## Slide 13: Tomahawk: MPSoC Architecture for LTE
- 3x 5.47 GBit/s
- 10x “LTE10”
- 10x 5.47 GBit/s
- 30x “LTE10”
- 4 MMAC/MHz
- 0.8 GMAC/s
@200MHz
- 1x “LTE10”
265 kB
1 MFLOP/MHz
3 MOPS/MHz
- 3x 5.47 GBit/s
- 10x “LTE10”
- 2x 5.47 GBit/s
- 7x “LTE10”
LTE10 - 10MBit/s DL scenario

## Slide 14: Tomahawk - Die Photo
10 mm
10 mm
- Taped out on May 7, 2007
- Returned on Aug 15,2007
& Jan 07, 2008
- UMC 130nm
8 metal layers
57 mil. transistors
40 GOPS @ 175MHz
12 Processors:
  2x RISC
  6x VDSP
  2x SDSP
  2x ASIP
On chip SRAM ~ 7.3 MBit
Notes: Return Datum

## Slide 15: Tomahawk: Area [mm²] and Power consumption [mW]
* Without implemented clock gating; Factor ½ reduction of power consumption by using clock gating
 |  | DC212GP | CoreManager | SDSP | 2x SDSP | VDSP | 6x VDSP | LDPC
AREA [mm2] | Logic | 1.10 | 2.60 | 0.25 | 0.50 | 0.65 | 3.90 | 2.10
 | Memory | 0.60 | 1.50 | 2.50 | 5.00 | 2.50 | 15.00 | 4.20
 | Post P&R | 2.50 | 5.90 | 3.30 | 6.60 | 3.80 | 22.80 | 7.50
Power [mW] | Simulated | 92.00 | 284.00* | 27.00 | 54.00 | 68.00 | 408.00 | 437.00
 | Measured | 30.00 | - | 26.00 | 52.00 | 84.00 | 504.00 | 354.00

## Slide 16: Area & Power Efficiency
MIMO SVD ASIC
Consumer RISC
Multimedia DSP
FFT Processor
RISC CPU with Media Processor
Communications DSP
CAM LSI
Video Stream Multi-Processor
Hearing Aid DSP
Source: Markovic et. al., Power and Area Minimization for Multidimensional Signal Processing, IEEE J. Solid-State
Circuits, vol. 42, no. 4, pp. 922-934, April 2007. Results scaled to 90 nm, operations are 12 bit add equivalents
1
2
3
4
5
6
7
8
9
by 1

## Slide 17: Performance Scalability
Scalability depends on:
  Task to scheduling time ratio,
  Inter-Task dependency
Baseband signal processing:
  Task execution time
  ~ 102 - 104 cycles
  SW scheduling
  ~ 103 cycles/task
  HW accelerated scheduling ~100 cycles/task
  CoreManager scheduling:
  60 cycles/task @100nJ
  RISC (DC212GP) scheduling:
  3000 cycles/task @ 500nJ
Measured for 0% or 50% task dependency
LTE symbol duration ~70us → 14000 cycles @ 200MHz
Effective time/symbol budget for N PEs → N . 14000 cycles

## Slide 18: Conclusions
Scalable self-scheduled MPSoC HW/SW solution possible
  For class of wireless communications applications
  For multi-media
  For …?
  But not for everything
Tomahawk Test Chip
  If scaled to 45nm CMOS: <200mW and <20mm2 LTE baseband feasible!